## Slide 1: FaultSim: A fast, configurable memory-resilience simulator
DAVID A. ROBERTS, AMD RESEARCH
PRASHANT J. NAIR, GEORGIA INSTITUTE OF TECHNOLOGY
{David.roberts@amd.com, pnair6@gatech.edu}
June 14th 2014

## Slide 2: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2014 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.

## Slide 3: MOTIVATION
Multi-granularity DRAM faults are common*
  Bit, column, row, bank or rank
3D die-stacking introduces through-silicon vias (TSVs) as new points of failure
ECC needs to be customized to the memory
  e.g. ECC-DIMM, ChipKill, RAID etc.
Complex to model analytically
  Including scrubbing & dynamic repair
REAL-WORLD MEMORY FAILURES
FaultSim allows quick & easy memory resilience design space exploration
*V. Sridharan and D. Liberty, “A study of dram failures in the field,” in
High Performance Computing, Networking, Storage and Analysis (SC), 2012 International Conference for, pp. 1–11, 2012.

## Slide 4: SIMULATOR
Memory chips (Fault Domains) organized into ranks (Domain Groups)
Monte Carlo randomized fault injection according to field study failure rates
  Divide chip lifetime into fixed intervals (e.g. 7 year lifetime with 3-hour intervals)
At each time step, Fault Ranges (FRs) randomly inserted into a list within each FD according to fault probability
  Evaluate ECC against recorded fault patterns

## Slide 5: FAULT REPRESENTATION
Example memory with 8 rows and 8 bits per row
  6-bit addresses
  Fault ranges A, B and C (A and B intersect)
  Mask field: indicates that fault address bit i can be 0 or 1 (covers both values)
  Address field: indicates specific address bit values where Maski == 0
FR | Mask | Address
A | 011000 | 000001
B | 000111 | 010000
C | 000111 | 110000

## Slide 6: FAULT range intersection
Identifying intersection of FRs is a fundamental operation of the simulator
  Allows detection of faults across chips in the same codeword(s)
  Fast O(1) boolean function
  FRs X and Y intersect if, for all address bit positions i
    Either one of the masks is 1 (fault covers 0 and 1 values) OR
    The specific address bits match
XY |  |  | Intersects?
AB | 011111 | 101110 | 1
AC | 011111 | 001110 | 0
BC | 000111 | 011111 | 0
+ == 1
Examples for potentially intersecting Fault Range combinations X and Y

## Slide 7: ECC EVALUATION ALGORITHM
We validate the simulator using conventional ECC-DIMM and ChipKill codes
  One DRAM rank composed of ‘18’ 4-bit wide (x4) DRAM chips
  Simulated results compared with approximate analytical model
FaultSim results for SECDED & ChipKill within 2% of approx. analytical model
Example: ChipKill ECC
  Count the maximum number of faulty symbols in any one codeword
  Assume 8-bit symbol size in following example
  Record a failure if faulty symbol count per codeword > 1

## Slide 8: Chipkill ECC algorithm example
Fault Domain (chip) states at end of time step
…
18 chips
In rank
CHIP 0
CHIP 1
Fault Range A
Fault Range B

## Slide 9: Chipkill ECC algorithm example
n_intersect
0
…
18 chips
In rank
CHIP 0
CHIP 1
FRtemp
Fault Range B
FR0 = A
FRtemp = FR0
Copy the starting FR (FR0) to a temporary FR

## Slide 10: Chipkill ECC algorithm example
Broaden FRtemp to cover the symbol width of 8 bits
Consider all FRs (including A) for intersection with symbol
Increment n_intersect when true
…
18 chips
In rank
CHIP 0
CHIP 1
FRtemp
Fault Range B
FR0 = A
FRtemp = FR0
FRtemp.mask |= 0x7
FR1 = A
If( intersects( FRtemp, FR1) ) n_intersect++
n_intersect
0
1

## Slide 11: Chipkill ECC algorithm example
Broaden FRtemp to cover the symbol width of 8 bits
Consider all FRs (including A) for intersection with symbol
Increment n_intersect when true
…
18 chips
In rank
CHIP 0
CHIP 1
FRtemp
Fault Range B
FR0 = A
FRtemp = FR0
FRtemp.mask |= 0x7
FR1 = A
If( intersects( FRtemp, FR1) ) n_intersect++
FR1 = B
If( intersects( FRtemp, FR1) ) n_intersect++
n_intersect
0
1
2
Exceeds correctable errors:
Stop simulation

## Slide 12: Chipkill ECC algorithm example
Continue algorithm from FR0 = B if n_intersect <= 1
Reset n_intersect = 0
Two loops are necessary because you may not have counted FR1’s that span more symbols*
…
18 chips
In rank
CHIP 0
CHIP 1
Fault Range B
FR0 = B
FRtemp = FR0
FRtemp.mask |= 0x7
FR1 = A
If( intersects( FRtemp, FR1) ) n_intersect++
FR1 = B
If( intersects( FRtemp, FR1) ) n_intersect++
n_intersect
0
1
2
Fault Range A
* See backup slide

## Slide 13: RESULTS AND FUTURE WORK
Simulated failure probability (BCH, ChipKill) within 2% of analytical model
Used FaultSim for evaluation in “Citadel” 3D-stacked DRAM ECC paper
We are continuing to develop the tool for new fault models, memory types and improved accuracy (real ECC evaluation and data patterns)
Intention to release an open-source version

## Slide 14: QUESTIONS?

## Slide 15: BACKUP
Add a third chip (CHIP 2)
Broadening FRB and FRC into FRtemp (symbol width) does not change their size
Starting from FR0 = C, you will see 2 intersections (Chips 2 and 1)
Starting from FR0 = A, you will see 3 intersections (Chips 1, 2 and 0)
Therefore every FR needs to be considered as FR0 to find greatest number of overlapping symbols in the rank
Explanation for use of two for loops
CHIP 0
CHIP 1
Fault Range B
Fault Range A
CHIP 2
Fault Range C