## Slide 1
Lecture 25: Synchronization, Consistency, VM
Today’s topics:
  Synchronization primitives
  Consistency models
  Virtual memory basics

## Slide 2
Snooping-Based Protocols
Three states for a block: invalid, shared, modified
A write is placed on the bus and sharers invalidate themselves
The protocols are referred to as MSI, MESI, etc.
Processor
Caches
Processor
Caches
Processor
Caches
Processor
Caches
Main Memory
I/O System

## Slide 3
Cache Coherence Protocols
Directory-based: A single location (directory) keeps track
of the sharing status of a block of memory
Snooping: Every cache block is accompanied by the sharing
status of that block – all cache controllers monitor the
shared bus so they can update the sharing status of the
block, if necessary
Write-invalidate: a processor gains exclusive access of
a block before writing by invalidating all other copies
Write-update: when a processor writes, it updates other
shared copies of that block

## Slide 4
Constructing Locks
Applications have phases (consisting of many instructions)
that must be executed atomically, without other parallel
processes modifying the data
A lock surrounding the data/code ensures that only one
program can be in a critical section at a time
The hardware must provide some basic primitives that
allow us to construct locks with different properties
Bank balance
$1000
Rd $1000
Add $100
Wr $1100
Rd $1000
Add $200
Wr $1200
Parallel (unlocked) banking transactions

## Slide 5
Synchronization
The simplest hardware primitive that greatly facilitates
synchronization implementations (locks, barriers, etc.)
is an atomic read-modify-write
Atomic exchange: swap contents of register and memory
Special case of atomic exchange: test & set: transfer
memory location into register and write 1 into memory
(if memory has 0, lock is free)
lock: t&s register, location
bnz register, lock
CS
st location, #0
When multiple parallel threads
execute this code, only one
will be able to enter CS

## Slide 6
Coherence Vs. Consistency
Coherence guarantees (i) write propagation
(a write will eventually be seen by other processors), and
(ii) write serialization (all processors see writes to the
same location in the same order)
The consistency model defines the ordering of writes and
reads to different memory locations – the hardware
guarantees a certain consistency model and the
programmer attempts to write correct programs with
those assumptions

## Slide 7
Consistency Example
Consider a multiprocessor with bus-based snooping cache
coherence
Initially A = B = 0
P1 P2
A  1 B  1
… …
if (B == 0) if (A == 0)
Crit.Section Crit.Section

## Slide 8
Consistency Example
Consider a multiprocessor with bus-based snooping cache
coherence
Initially A = B = 0
P1 P2
A  1 B  1
… …
if (B == 0) if (A == 0)
Crit.Section Crit.Section
The programmer expected the
above code to implement a
lock – because of ooo, both processors
can enter the critical section
The consistency model lets the programmer know what assumptions
they can make about the hardware’s reordering capabilities

## Slide 9
Sequential Consistency
A multiprocessor is sequentially consistent if the result
of the execution is achievable by maintaining program
order within a processor and interleaving accesses by
different processors in an arbitrary fashion
The multiprocessor in the previous example is not
sequentially consistent
Can implement sequential consistency by requiring the
following: program order, write serialization, everyone has
seen an update before a value is read – very intuitive for
the programmer, but extremely slow

## Slide 10
Relaxed Consistency
Sequential consistency is very slow
The programming complications/surprises are caused when the
program has race conditions (two threads dealing with same
data and at least one of the threads is modifying the data)
If programmers are disciplined and enforce mutual exclusion
when dealing with shared data, we can allow some re-orderings
and higher performance
This is effective at balancing performance & programming effort

## Slide 11
Virtual Memory
Processes deal with virtual memory – they have the
illusion that a very large address space is available to
them
There is only a limited amount of physical memory that is
shared by all processes – a process places part of its
virtual memory in this physical memory and the rest is
stored on disk (called swap space)
Thanks to locality, disk access is likely to be uncommon
The hardware ensures that one process cannot access
the memory of a different process

## Slide 12
Virtual Memory

## Slide 13
Address Translation
The virtual and physical memory are broken up into pages
Virtual address
8KB page size
page offset
virtual page
number
Translated to physical
page number
Physical address
13

## Slide 14
Memory Hierarchy Properties
A virtual memory page can be placed anywhere in physical
memory (fully-associative)
Replacement is usually LRU (since the miss penalty is
huge, we can invest some effort to minimize misses)
A page table (indexed by virtual page number) is used for
translating virtual to physical page number
The page table is itself in memory