## Slide 1
Lecture 2: Metrics to Evaluate Systems
Topics: Metrics: power, energy, reliability, cost, performance,
summarizing performance with AM, GM, HM
My email: rajeev@cs
TA office hour details on class webpage
HW1 posted later today, due Wed Aug 31st (note auto extension)
Lecture break
Class resources (notes)

## Slide 2
Where Are We Headed?
Modern trends:
  Clock speed improvements are slowing (power constraints)
  Difficult to further optimize a single core for performance
  Multi-cores: each new processor generation will
  accommodate more cores
  Need better programming models and efficient
  execution for multi-threaded applications
  Reduced data movement
  Need better memory hierarchies
  Need greater energy efficiency
  Dark silicon, accelerators
  Emergence of new workloads: ML, graphs, genomics
  Emergence of new metrics: security, reliability

## Slide 3
Power Consumption Trends
Dyn power a activity x capacitance x voltage2 x frequency
Capacitance per transistor and voltage are decreasing, but
number of transistors is increasing at a faster rate, and Dennard
scaling has ended; hence clock frequency must be kept steady
Leakage power is also rising; is a function of transistor
count, leakage current, and supply voltage
Power consumption is already between 100-150W in
high-performance processors today
Energy = power x time = (dynpower + lkgpower) x time

## Slide 4
Problem 1
For a processor running at 100% utilization at 100 W,
20% of the power is attributed to leakage. What is the
total power dissipation when the processor is running at
50% utilization?

## Slide 5
Problem 1
For a processor running at 100% utilization at 100 W,
20% of the power is attributed to leakage. What is the
total power dissipation when the processor is running at
50% utilization?
Total power = dynamic power + leakage power
= 80W x 50% + 20W
= 60W
Solve for 0% utilization; the system consumes 20W.
This is the basis for “server consolidation” in datacenters
(move processes so you have a few highly utilized servers).

## Slide 6
Power Vs. Energy
Energy tells us the true “cost” of performing a fixed task
Power (energy/time) poses constraints; can only work fast
enough to max out the power delivery or cooling solution
If processor A consumes 1.2x the power of processor B,
but finishes the task in 30% less time, its relative energy
is 1.2 X 0.7 = 0.84; Proc-A is better, assuming that 1.2x
power can be supported by the system

## Slide 7
Problem 2
If processor A consumes 1.4x the power of processor B,
but finishes the task in 20% less time, which processor
would you pick:
(a) if you were constrained by power delivery constraints?
(b) if you were trying to minimize energy per operation?
(c) if you were trying to minimize response times?

## Slide 8
Problem 2
If processor A consumes 1.4x the power of processor B,
but finishes the task in 20% less time, which processor
would you pick:
(a) if you were constrained by power delivery constraints?
Proc-B
(b) if you were trying to minimize energy per operation?
Proc-A is 1.4x0.8 = 1.12 times the energy of Proc-B
(c) if you were trying to minimize response times?
Proc-A is faster, but we could scale up the frequency
(and power) of Proc-B and match Proc-A’s response
time (while still doing better in terms of power and
energy) (only if the circuits can handle the faster clock)

## Slide 9
Reducing Power and Energy
Can gate off transistors that are inactive (reduces leakage)
Design for typical case and throttle down when activity
exceeds a threshold
DFS: Dynamic frequency scaling -- only reduces frequency
and dynamic power, but hurts energy
DVFS: Dynamic voltage and frequency scaling – can reduce
voltage and frequency by (say) 10%; can slow a program
by (say) 8%, but reduce dynamic power by 27%, reduce
total power by (say) 23%, reduce total energy by 17%
(Note: voltage drop  slow transistor  freq drop)

## Slide 10
Problem 3
Processor-A at 3 GHz consumes 80 W of dynamic power
and 20 W of static power. It completes a program in 20
seconds.
What is the energy consumption if I scale frequency down
by 20%?
What is the energy consumption if I scale frequency and
voltage down by 20%?

## Slide 11
Problem 3
Processor-A at 3 GHz consumes 80 W of dynamic power
and 20 W of static power. It completes a program in 20
seconds.
What is the energy consumption if I scale frequency down
by 20%?
New dynamic power = 64W; New static power = 20W
New execution time = 25 secs (assuming CPU-bound)
Energy = 84 W x 25 secs = 2100 Joules
What is the energy consumption if I scale frequency and
voltage down by 20%?
New dynamic power = 41W; New static power = 16W;
New exec time = 25 secs; Energy = 1425 Joules

## Slide 12
Other Technology Trends
DRAM density increases by 40-60% per year, latency has
reduced by 33% in 10 years (the memory wall!), bandwidth
improves twice as fast as latency decreases
Disk density improves by 100% every year, latency
improvement similar to DRAM
Emergence of NVRAM technologies that can provide a
bridge between DRAM and hard disk drives
Also, growing concerns over reliability (since transistors
are smaller, operating at low voltages, and there are so
many of them)

## Slide 13
Defining Reliability and Availability
A system toggles between
  Service accomplishment: service matches specifications
  Service interruption: services deviates from specs
The toggle is caused by failures and restorations
Reliability measures continuous service accomplishment
and is usually expressed as mean time to failure (MTTF)
Availability measures fraction of time that service matches
specifications, expressed as MTTF / (MTTF + MTTR)

## Slide 14
Cost
Cost is determined by many factors: volume, yield,
manufacturing maturity, processing steps, etc.
One important determinant: area of the chip
Small area  more chips per wafer
Small area  one defect leads us to discard a small-area
chip, i.e., yield goes up
Roughly speaking, half the area  one-third the cost