## Slide 1
Lecture: Large Caches, Virtual Memory
Topics: cache innovations, large caches, virtual memory intro

## Slide 2
Types of Cache Misses
Compulsory misses: happens the first time a memory
word is accessed – the misses for an infinite cache
Capacity misses: happens because the program touched
many other words before re-touching the same word – the
misses for a fully-associative cache
Conflict misses: happens because two words map to the
same location in the cache – the misses generated while
moving from a fully-associative to a direct-mapped cache
Sidenote: can a fully-associative cache have more misses
than a direct-mapped cache of the same size?

## Slide 3
More Cache Basics
L1 caches are split as instruction and data; L2 and L3
are unified
The L1/L2 hierarchy can be inclusive, exclusive, or
non-inclusive
On a write, you can do write-allocate or write-no-allocate
On a write, you can do writeback or write-through;
write-back reduces traffic, write-through simplifies coherence
Reads get higher priority; writes are usually buffered
L1 does parallel tag/data access; L2/L3 does serial tag/data

## Slide 4
Tolerating Miss Penalty
Out of order execution: can do other useful work while
waiting for the miss – can have multiple cache misses
-- cache controller has to keep track of multiple
outstanding misses (non-blocking cache)
Hardware and software prefetching into prefetch buffers
– aggressive prefetching can increase contention for buses

## Slide 5
Reducing Miss Rate
Large block size – reduces compulsory misses, reduces
miss penalty in case of spatial locality – increases traffic
between different levels, space waste, and conflict misses
Large cache – reduces capacity/conflict misses – access
time penalty
High associativity – reduces conflict misses – rule of thumb:
2-way cache of capacity N/2 has the same miss rate as
1-way cache of capacity N – more energy

## Slide 6
Techniques to Reduce Cache Misses
Victim caches
Better replacement policies – pseudo-LRU, NRU, DRRIP
-- insertion, promotion, victim selection
Prefetching, cache compression

## Slide 7
Victim Caches
A direct-mapped cache suffers from misses because
multiple pieces of data map to the same location
The processor often tries to access data that it recently
discarded – all discards are placed in a small victim cache
(4 or 8 entries) – the victim cache is checked before going
to L2
Can be viewed as additional associativity for a few sets
that tend to have the most conflicts

## Slide 8
Replacement Policies
Pseudo-LRU: maintain a tree and keep track of which
side of the tree was touched more recently; simple bit ops
NRU: every block in a set has a bit; the bit is made zero
when the block is touched; if all are zero, make all one;
a block with bit set to 1 is evicted

## Slide 9
Prefetching
Hardware prefetching can be employed for any of the
cache levels
It can introduce cache pollution – prefetched data is
often placed in a separate prefetch buffer to avoid
pollution – this buffer must be looked up in parallel
with the cache access
Aggressive prefetching increases “coverage”, but leads
to a reduction in “accuracy”  wasted memory bandwidth
Prefetches must be timely: they must be issued sufficiently
in advance to hide the latency, but not too early (to avoid
pollution and eviction before use)

## Slide 10
Stream Buffers
Simplest form of prefetch: on every miss, bring in
multiple cache lines
When you read the top of the queue, bring in the next line
L1
Stream buffer
Sequential lines

## Slide 11
Stride-Based Prefetching
For each load, keep track of the last address accessed
by the load and a possibly consistent stride
FSM detects consistent stride and issues prefetches
init
trans
steady
no-pred
incorrect
correct
incorrect
(update stride)
correct
correct
correct
incorrect
(update stride)
incorrect
(update stride)
tag
prev_addr
stride
state
PC

## Slide 12
Shared Vs. Private Caches in Multi-Core
What are the pros/cons of a shared L2 cache?
P4
P3
P2
P1
L1
L1
L1
L1
L2
L2
L2
L2
P4
P3
P2
P1
L1
L1
L1
L1
L2

## Slide 13
Shared Vs. Private Caches in Multi-Core
Advantages of a shared cache:
  Space is dynamically allocated among cores
  No waste of space because of replication
  Potentially faster cache coherence (and easier to
  locate data on a miss)
Advantages of a private cache:
  small L2  faster access time
  private bus to L2  less contention

## Slide 14
UCA and NUCA
The small-sized caches so far have all been uniform cache
access: the latency for any access is a constant, no matter
where data is found
For a large multi-megabyte cache, it is expensive to limit
access time by the worst case delay: hence, non-uniform
cache architecture

## Slide 15
Large NUCA
CPU
Issues to be addressed for
Non-Uniform Cache Access:
  Mapping
  Migration
  Search
  Replication

## Slide 16
Core 0
L1
D$
L1
I$
L2 $
Core 1
L1
D$
L1
I$
L2 $
Core 2
L1
D$
L1
I$
L2 $
Core 3
L1
D$
L1
I$
L2 $
Core 4
L1
D$
L1
I$
L2 $
Core 5
L1
D$
L1
I$
L2 $
Core 6
L1
D$
L1
I$
L2 $
Core 7
L1
D$
L1
I$
L2 $
Memory Controller for off-chip access
A single tile composed
of a core, L1 caches, and
a bank (slice) of the
shared L2 cache
The cache controller
forwards address requests
to the appropriate L2 bank
and handles coherence
operations
Shared NUCA Cache

## Slide 17
Virtual Memory
Processes deal with virtual memory – they have the
illusion that a very large address space is available to
them
There is only a limited amount of physical memory that is
shared by all processes – a process places part of its
virtual memory in this physical memory and the rest is
stored on disk
Thanks to locality, disk access is likely to be uncommon
The hardware ensures that one process cannot access
the memory of a different process

## Slide 19
Address Translation
The virtual and physical memory are broken up into pages
Virtual address
8KB page size
page offset
virtual page
number
Translated to phys
page number
Physical memory
13
Physical address
page offset
physical page
number
13

## Slide 20
Problem 1
Assume a large shared LLC that is tiled and distributed on the chip.
Assume 16 tiles. Assume an OS page size of 8KB. The entire LLC
has a size of 32 MB, uses 64-byte blocks, and is 8-way set-associative.
Which of the 40 physical address bits are used to specify the tile number?
Provide an example page number that is assigned to tile 0.

## Slide 21
Problem 1
Assume a large shared LLC that is tiled and distributed on the chip.
Assume 16 tiles. Assume an OS page size of 8KB. The entire LLC
has a size of 32 MB, uses 64-byte blocks, and is 8-way set-associative.
Which of the 40 physical address bits are used to specify the tile number?
Provide an example page number that is assigned to tile 0.
The cache has 64K sets, i.e., 6 block offset bits, 16 index bits, and
18 tag bits. The address also has a 13-bit page offset, and 27 page
number bits. Nine bits (bits 14-22) are used for the page number and
the index bits. Any four of those bits can be used to designate the tile
number, say, bits 19-22. An example page number assigned to tile 0
is xxx…xxx0000xxx…xxx
bit 22 19
40 Tag 23
22 Index 7
6 Offset 1
40 Page number 14
13 Page offset 1

## Slide 22
Memory Hierarchy Properties
A virtual memory page can be placed anywhere in physical
memory (fully-associative)
Replacement is usually LRU (since the miss penalty is
huge, we can invest some effort to minimize misses)
A page table (indexed by virtual page number) is used for
translating virtual to physical page number
The memory-disk hierarchy can be either inclusive or
exclusive and the write policy is writeback